## Slide 2
About the Assembly
A smart lab based out of In5 since Dec 2014
Over 200 free workshops done
ASSEMBLY: HACK - Embedded systems, iOT and hardware
ASSEMBLY: CODE - Software projects - APIs, frameworks, apps
Age range: 16-60 - students, professionals, entrepreneurs
Focus on smart technology and practical applications
Forum: members.theassembly.ae

## Slide 3
TAG US ON OUR SOCIAL MEDIA
The Assembly (@MakeSmartThings)
@MakeSmartThings
@MakeSmartThings
The Assembly
FACEBOOK
TWITTER
INSTAGRAM
YOUTUBE

## Slide 4
Agenda
Magnetic Levitation - What is it?
Real life applications
The design
Components
  Neodymium magnets
  Arduino UNO
  Transistor
  Electromagnet
  Linear hall effect sensor
How it Works
Arduino IDE Code
  Without PID
  With PID

## Slide 5: Magnetic Levitation

## Slide 6: Real life applications
Maglev transportation
Levitation melting
Toys

## Slide 7
Shanghai
Maglev
Fastest Commercial train in the world!

## Slide 8
Top Speed: 431 km/h (267 mph)
Reaches 354 km/h in 2 minutes
Cost: 546 million AED over 2.5 years
30.5 km long track
Takes 7 min & 20 seconds to complete journey
Uses magnetic levitation!

## Slide 9: Dubai metro only has a max of 90 km/h and takes 2.4 hrs to finish 75 km (red line)
It’s slower

## Slide 11
The magnets are superconducting, when cooled to less than 450 degree below zero, they generate magnetic fields strong enough to suspend and propel a train

## Slide 12
1. USA (2013 – present) Train: Hyperloop project Speed: 1,200 km/h – 745 mph Capacity: Experimental
2. Japan (2002 – present) Train: JR-Maglev MLX01 Speed: 581 km/h – 361 mph Capacity: Experimental
3. France (2000 – 2007) Train: TGV V150 Speed: 574 km/h – 357 mph Capacity: Experimental
4. Germany (1987 – 2012) Train: Transrapid TR-07 Speed: 434 km/h – 270.3 mph Capacity: Experimental

## Slide 13: Levitation melting
Notes: With levitation melting, induction energy creates a force strong enough within theinduction coil to allow to counter gravity. The metal part remains in the inductionfield and heats until it has melted. Levitation melting is ideal for industries that need pure samples, without potential contamination from a crucible.

## Slide 14
Video Link:
https://www.youtube.com/watch?v=VydPQuLyEns

## Slide 15: Toys!

## Slide 16: Body Design
Electromagnet
Hall effect Sensor
Vertical Design
Neck, mount and base are 3D printed
The Electromagnet pole is face down
The Hall effect sensor is placed face down, approximately 5mm from the Electromagnet

## Slide 17
A stick held from the bottom is unstable. Once it starts to tip, gravity will tend to make it tip more. Only by reacting and moving your hand can you hold it upright
A stick held from the top is naturally stable. Push the bottom off-center, and gravity tends to pull it back to the stable position.

## Slide 18: Designs utilizing levitation from the bottom

## Slide 19
Witchcraft!?

## Slide 20
The four copper windings around steel shafts are electromagnets.
Hall effect sensors, highlighted in yellow

## Slide 21: How it levitates

## Slide 23: Components

## Slide 24
  Neodymium magnets
  Arduino UNO
  Transistor
  Electromagnet
  Linear hall effect sensor

## Slide 25: Neodymium magnets (NdFeB or Neo magnet)
Rare earth magnet (permanent magnets made from alloys of rare-earth elements)
Strongest permanent magnets commercially available.
Developed independently in 1982 by General Motors and Sumitomo Special Metals,

## Slide 26: Electromagnet
It is a magnet that runs on electricity. The strength of an electromagnet can easily be changed by changing the amount of electric current that flows through it. The poles of an electromagnet can even be reversed by reversing the flow of electricity.
More turns = stronger magnetic field (flux density)

## Slide 27: Arduino UNO
Arduino is an open-source platform used for building electronics projects. It consists of both a physical programmable circuit board (a microcontroller) and a piece of software, that runs on your computer.
UNO: 6 analog input pins, 14 I/O digital ports that are used to connect with external electronic circuits. Out of 14 I/O ports, 6 pins can be used for PWM output.

## Slide 28
Used to measure the magnitude of a magnetic field
output voltage is directly proportional to the magnetic field.
Hall effect sensors are used for proximity sensing, positioning, speed detection, and current sensing applications.
Linear hall effect sensor

## Slide 29: Hall effect

## Slide 30: Transistor
Semiconductors able to change from conductor to insulator
Can either allow or prohibit current flow
Uses: amplifiers, switch, voltage regulation, etc.
B
C
E

## Slide 31: The Circuit

## Slide 32: Hall sensor and Arduino Connection

## Slide 33: Transistor and Electromagnet

## Slide 35: The Code behind it all

## Slide 36: Simple If – Else Code
GitHub link - https://github.com/The-Assembly/Magnetic_Levitation
Download file – levitator_ino_workshop.ino
Open it on Arduino IDE and Run it

## Slide 37: Fun Challenge
Find the setpoint by youself!
Hint – 300 < x < 400

## Slide 38: But there is a problem!

## Slide 39: PID Controller

## Slide 41: How PID Controller works

## Slide 42: Download PID code on GitHub
GitHub link - https://github.com/The-Assembly/Magnetic_Levitation
Download file – levitator_pid_ino.ino
Run in Arduino IDE

## Slide 43: PID Tuning Method
Set all values to zero.
Increase the P value until the response to a disturbance is steady oscillation.
Increase the D value until the the oscillations go away (i.e. it's critically damped).
Repeat steps 2 and 3 until increasing the D value does not stop the oscillations.
Set P and D to the last stable values.
Increase the I gain until it brings you to the setpoint with the number of oscillations desired (normally zero)

## Slide 44: Fun Challenge
Find PID Values by yourself
Hint:-
0 < Kp < 3
0 < Ki < 0.5
0 < Kd < 0.5

## Slide 45: PID Spoiler Alert
Kp = 2
Ki = 0.11
Kd = 0.1

## Slide 46: Next workshop teaser - Closing